## Slide 1: Raster operations
Geomathematics, programming and geoinformatics
2026.03.11.
Ákos Bede-Fazekas

## Slide 2: Raster operations
menu
  some important tools are also available here
  but far from all of them
Processing Toolbox
  QGIS native tools
  GDAL, GRASS and SAGA tools

## Slide 3: Raster operations
many tools, scattered around
  their names are not always descriptive
  the Hungarian translation is sometimes unusual
use the search!
DEMO
  which is the tool that calculates the shade on the terrain for an elevation raster (DEM)

## Slide 4: Raster operations
many tools, scattered around
  their names are not always descriptive
  the Hungarian translation is sometimes unusual
use the search!
DEMO
  which is the tool that calculates the shade on the terrain for an elevation raster (DEM)
solution: Raster terrain analysis > Hillshade

## Slide 5: Characteristics derived from elevation
contour line / contour polygon
slope
aspect
hillshade
topographic position (TPI)
terrain ruggedness / roughness (TRI, roughness)
curvature

## Slide 6: Characteristics derived from elevation
contour line / contour polygon
slope
aspect
hillshade
topographic position (TPI)
terrain ruggedness / roughness (TRI, roughness)
curvature
– WE'LL TRY THESE OUT –

## Slide 7: Slope
slope
Raster terrain analysis > Slope
calculates the slope angle (in degrees)
  this can later be converted to radians or slope percent
  and slope categories can be created from degrees or percentages
Notes: Raszteres terepelemzés > Lejtőszög

## Slide 8: Slope
slope
Raster terrain analysis > Slope
calculates the slope angle (in degrees)
  this can later be converted to radians or slope percent
  and slope categories can be created from degrees or percentages
– RECLASSIFY –
– RASTER CALCULATOR –

## Slide 9: Slope
slope
Raster terrain analysis > Slope
calculates the slope angle (in degrees)
  this can later be converted to radians or slope percent
  and slope categories can be created from degrees or percentages
DEMO
  calculate the slope from the digital elevation model
  modify the color ramp
– RECLASSIFY –
– RASTER CALCULATOR –

## Slide 10: Aspect
aspect
two tools with fairly similar behaviour
  Raster terrain analysis > Aspect
  GDAL > Raster analysis > Aspect
the direction the slope faces
  more precisely: the horizontal projection of the slope direction
  in other words: the opposite direction of the incoming light ray perpendicular to the surface
the result is in degrees (or radians)
  0°/360°: north, 90°: east, 180°: south, 270°: west
  completely flat areas are conventionally NoData/0/-1
Notes: Raszteres terepelemzés > Kitettség
GDAL > Raszteranalízis > Kitettség

## Slide 11: Aspect
DEMO
  create an aspect raster from the digital elevation model
  assign an orange color to cells with unknown values (i.e. flat areas) (Transparency section)

## Slide 12: Aspect
usually colored with a red–yellow–turquoise–dark blue–red color ramp
  either continuously or divided into 4/8 categories
can be combined with slope

## Slide 13: Aspect
usually colored with a red–yellow–turquoise–dark blue–red color ramp
  either continuously or divided into 4/8 categories
can be combined with slope

## Slide 14: Aspect
usually colored with a red–yellow–turquoise–dark blue–red color ramp
  either continuously or divided into 4/8 categories
can be combined with slope

## Slide 15: Hillshade
hillshade
two tools
  Raster terrain analysis > Hillshade
  GDAL > Raster analysis > Hillshade
  the latter offers slightly more settings
we must define the direction of the incoming sunlight (azimuth and altitude angle)
a cartographic convention is that the sun shines from the northwest (300–315°)
  as if we were in the southern hemisphere
  this produces a nicer result than illumination from the south
Notes: Raszteres terepelemzés > Domborzatárnyékolás
GDAL > Raszteranalízis > Domborzatárnyékolás

## Slide 16: Hillshade
DEMO
  create a hillshade raster using the QGIS native tool
  set the transparency of the new layer to 50%, and color the elevation model below it

## Slide 17: Hillshade
hillshading and contour visualization can also be enabled in the Symbology settings
  in this case no new raster is created
  we only display the existing digital elevation model differently

## Slide 18: Additional raster tools
resampling, aggregation, disaggregation
  SAGA > Raster – Tools > Resampling
  GRASS > Raster > r.resample / r.resamp.interp
masking
  SAGA > Raster – Tools > Raster masking
distance calculation
  GDAL > Raster analysis > Proximity (raster distance)
creating constant and random rasters
  Raster creation > Create constant raster layer
  Raster creation > Create random raster layer (uniform distribution)
Notes: SAGA > Raster – Tools > Resampling
GRASS > Raster > r.resample / r.resamp.interp
SAGA > Raster – Tools > Raster masking
GDAL > Raszteranalízis > Közelség (raszter távolság)
Raszterkészítés > Konstans raszterréteg létrehozása
Raszterkészítés > Véletlenszerű raszterréteg létrehozása (egyenletes eloszlás)

## Slide 19: Additional raster tools
mosaicking raster tiles
  GRASS > Imagery > i.image.mosaic
hydrological operations (filling local depressions, flow direction, watershed delineation)
  SAGA > Terrain Analysis – Preprocessing
  SAGA > Terrain Analysis – Hydrology
  GRASS > Raster > r.flow / r.water.outlet
reclassification
  Raster analysis > Reclassify by table
Notes: GRASS > Imagery > i.image.mosaic
SAGA > Terrain Analysis – Preprocessing
SAGA > Terrain Analysis – Hydrology
GRASS > Raster > r.flow / r.water.outlet
Raszteranalízis > Újraosztályozás tábla alapján
Raszteranalízis > Raster calculator

## Slide 20: Cell-by-cell operations between rasters
raster calculator, raster algebra, map algebra
Raster analysis > Raster calculator
operations between multiple rasters or raster bands
  for example adding or multiplying rasters
performed between cells located at the same position
operations can be
  mathematical (e.g. +, –, *, /)  numeric raster
  logical (e.g. >, >=, =)  logical raster (0/1)
the operands in the operation can be
  rasters
  numbers (~ constant rasters)
Notes: Raszteranalízis > Raster calculator

## Slide 21: Cell-by-cell operations between rasters
layers (@1, @2 etc.)
operators
expression
reference layer
output

## Slide 22: Cell-by-cell operations between rasters
layers (@1, @2 etc.)
operators
expression
reference layer
output

## Slide 23: Cell-by-cell operations between rasters
layers (@1, @2 etc.)
operators
expression
reference layer
output

## Slide 24: Cell-by-cell operations between rasters
layers (@1, @2 etc.)
operators
expression
reference layer
output

## Slide 25: Cell-by-cell operations between rasters
layers (@1, @2 etc.)
operators
expression
reference layer
output

## Slide 26: Cell-by-cell operations between rasters
layers (@1, @2 etc.)
operators
expression
reference layer
output
1

## Slide 27: Cell-by-cell operations between rasters
DEMO
  calculate slope percent from slope angle
  tan(degree * π / 180) * 100
  pay attention to the decimal separator!
  use the slope raster as the reference raster
tan("slope@1" * 3.14 / 180) * 100

## Slide 28: Cell-by-cell operations between rasters
DEMO
  create a new logical raster
  which is true (1) where the terrain has an eastern aspect (>45° AND <135°)
  and false (0) elsewhere
  color the true cells with a bright color and the false cells as transparent (Paletted / Unique values)
"aspect@1" > 45 AND "aspect@1" < 135

## Slide 29: Cell-by-cell operations between rasters
DEMO
  create a new elevation raster which
  increases elevation by 1.5× in flat areas (slope <5°)
  and leaves it unchanged elsewhere
  then create another raster representing the difference between the original and the increased elevation
"elevation@1" + ( "slope@1" < 5 ) * 0.5 * "elevation@1"
"higher@1" - "elevation@1"

## Slide 30: Practice exercise
create an alternative aspect raster that
  contains the value -1 where slope is lower than 3°
  and keeps the original aspect value elsewhere
  try to choose a suitable color scheme (►)

## Slide 31: Practice exercise
create an alternative aspect raster that
  contains the value -1 where slope is lower than 3°
  and keeps the original aspect value elsewhere
  try to choose a suitable color scheme (►)
solution:
("slope@1" < 3) * -1 + ("slope@1" >= 3) * "aspect@1"

## Slide 32: Thank you for your attention!
questions?