## Slide 1: Map layout
Geomathematics, programming and geoinformatics
2026.03.11.
Ákos Bede-Fazekas

## Slide 2: Print layout, map composition interface

## Slide 3: Print layouts
Project > Layout Manager…
  open previously created layouts
  create a new one
Notes: Projekt > Elrendezéskezelő…

## Slide 4: Print layouts
Project > Layout Manager…
  open previously created layouts
  create a new one

## Slide 5: Print layouts
Project > Layout Manager…
  open previously created layouts
  create a new one

## Slide 6: Print layouts
Project > Layout Manager…
  open previously created layouts
  create a new one
DEMO
  create a new print layout

## Slide 7: Map composition interface
add new item
overview of existing items
customize the selected item
navigation and selection
export
aligning and grouping items

## Slide 8: Map composition interface
add new item
overview of existing items
customize the selected item
navigation and selection
export
aligning and grouping items

## Slide 9: Map composition interface
add new item
overview of existing items
customize the selected item
navigation and selection
export
aligning and grouping items

## Slide 10: Map composition interface
add new item
overview of existing items
customize the selected item
navigation and selection
export
aligning and grouping items

## Slide 11: Map composition interface
add new item
overview of existing items
customize the selected item
navigation and selection
export
aligning and grouping items

## Slide 12: Map composition interface
add new item
overview of existing items
customize the selected item
navigation and selection
export
aligning and grouping items

## Slide 13: Map composition interface
add new item
overview of existing items
customize the selected item
navigation and selection
export
aligning and grouping items

## Slide 14: Map composition interface
add new item
overview of existing items
customize the selected item
navigation and selection
export
aligning and grouping items
and of course the most important:
  the print layout

## Slide 15: Map composition interface
DEMO
  add a map and a scale bar to the print layout
  select the map to view the item properties

## Slide 16: Exporting the map
the map can be sent to the printer
or saved as
  raster image (PNG, JPG, TIF, BMP etc.)
  vector graphic (SVG)
  PDF document
available from the menu or the toolbar

## Slide 17: Exporting the map
the map can be sent to the printer
or saved as
  raster image (PNG, JPG, TIF, BMP etc.)
  vector graphic (SVG)
  PDF document
available from the menu or the toolbar

## Slide 18: Exporting the map
the map can be sent to the printer
or saved as
  raster image (PNG, JPG, TIF, BMP etc.)
  vector graphic (SVG)
  PDF document
available from the menu or the toolbar

## Slide 19: Exporting the map
the map can be sent to the printer
or saved as
  raster image (PNG, JPG, TIF, BMP etc.)
  vector graphic (SVG)
  PDF document
available from the menu or the toolbar
DEMO
  save it as a PNG image
  with 600 dpi resolution

## Slide 20: Saving the print layout
do not forget to save the project occasionally
  and thus also the print layout
DEMO
  save

## Slide 21: Layout items

## Slide 22: Layout items
map
3D Map
picture: simple image
label: text box, e.g. for a title
legend
scale bar
north arrow
Notes: térkép
3D térkép
kép
címke
jelmagyarázat
lépték
északjel

## Slide 23: Layout items
shape: rectangle/ellipse/triangle
marker: point symbol
arrow
node item: polygon or polyline
HTML: formatted text
attribute table
fixed table: simple table
Notes: alak
szimbólum
nyíl
csomópont elem
HTML
attribútumtábla
fix táblázat

## Slide 24: North arrow, scale bar
common properties of the scale bar and north arrow
  linked map
  size
  background, frame, position
  name
additional properties of the scale bar
  style (ticks, black–white rectangles, stepped etc.)
  unit
  segments
additional properties of the north arrow
  shape (raster image or SVG)

## Slide 25: North arrow, scale bar
DEMO
  add a white background (Background) and a black frame (Frame) to the scale bar
  increase the margin to 3 mm (Display)
  rename it to "scale bar" (Items)
  set the unit to km (Units)
  construct it from four main segments of 0.5 km with subdivisions between them (Segments), using the "Line Ticks Up" style (Main Properties)
Notes: Térképtippek

## Slide 26: North arrow, scale bar
DEMO
  add a north arrow to the layout
  as the symbol, select the raster image north arrow.jpg
  make sure it is also linked to our map (Image Rotation)
Notes: Térképtippek

## Slide 27: Map
main buttons
  refresh
  copy extent/scale from or to the editing interface ("Main Canvas")
  "Interactively Edit Map Extent": zoom enabled
main properties
  scale and rotation
  lock layer visibility and style (no further synchronization)
  extent
  grid, frame and coordinate annotations
Notes: "fő vászon"
"térképterjedelem interaktív szerkesztése"

## Slide 28: Map
main buttons
  refresh
  copy extent/scale from or to the editing interface ("Main Canvas")
  "Interactively Edit Map Extent": zoom enabled
main properties
  scale and rotation
  lock layer visibility and style (no further synchronization)
  extent
  grid, frame and coordinate annotations
Notes: "fő vászon"
"térképterjedelem interaktív szerkesztése"

## Slide 29: Map
main buttons
  refresh
  copy extent/scale from or to the editing interface ("Main Canvas")
  "Interactively Edit Map Extent": zoom enabled
main properties
  scale and rotation
  lock layer visibility and style (no further synchronization)
  extent
  grid, frame and coordinate annotations
Notes: "fő vászon"
"térképterjedelem interaktív szerkesztése"

## Slide 30: Map
main buttons
  refresh
  copy extent/scale from or to the editing interface ("Main Canvas")
  "Interactively Edit Map Extent": zoom enabled
main properties
  scale and rotation
  lock layer visibility and style (no further synchronization)
  extent
  grid, frame and coordinate annotations
Notes: "fő vászon"
"térképterjedelem interaktív szerkesztése"

## Slide 31: Map
main buttons
  refresh
  copy extent/scale from or to the editing interface ("Main Canvas")
  "Interactively Edit Map Extent": zoom enabled
main properties
  scale and rotation
  lock layer visibility and style (no further synchronization)
  extent
  grid, frame and coordinate annotations
Notes: "fő vászon"
"térképterjedelem interaktív szerkesztése"

## Slide 32: Map
main buttons
  refresh
  copy extent/scale from or to the editing interface ("Main Canvas")
  "Interactively Edit Map Extent": zoom enabled
main properties
  scale and rotation
  lock layer visibility and style (no further synchronization)
  extent
  grid, frame and coordinate annotations
Notes: "fő vászon"
"térképterjedelem interaktív szerkesztése"

## Slide 33: Map
main buttons
  refresh
  copy extent/scale from or to the editing interface ("Main Canvas")
  "Interactively Edit Map Extent": zoom enabled
main properties
  scale and rotation
  lock layer visibility and style (no further synchronization)
  extent
  grid, frame and coordinate annotations
Notes: "fő vászon"
"térképterjedelem interaktív szerkesztése"

## Slide 34: Map
main buttons
  refresh
  copy extent/scale from or to the editing interface ("Main Canvas")
  "Interactively Edit Map Extent": zoom enabled
main properties
  scale and rotation
  lock layer visibility and style (no further synchronization)
  extent
  grid, frame and coordinate annotations
Notes: "fő vászon"
"térképterjedelem interaktív szerkesztése"

## Slide 35: Map – grid, frame and coordinates
multiple grids can be defined
  e.g. main and secondary grid (thick + thin)
  or according to different coordinate systems (WGS-84 and national)
the "grid" consists of three components (these can be switched on/off independently):
  grid or crosses
  frame ("zebra", line with ticks, simple line)
  coordinate annotations
Notes: "rács"

## Slide 36: Map – grid, frame and coordinates
grid properties
  type
  coordinate reference system
  interval and its unit
  style
frame properties
  type ("zebra", line with ticks, simple line)
  style settings
coordinate annotation properties
  format: decimal, DM, DMS; with or without suffix
  per side: display or not, outside/inside, rotation
  number of decimal places

## Slide 37: Map – grid, frame and coordinates
grid properties
  type
  coordinate reference system
  interval and its unit
  style
frame properties
  type ("zebra", line with ticks, simple line)
  style settings
coordinate annotation properties
  format: decimal, DM, DMS; with or without suffix
  per side: display or not, outside/inside, rotation
  number of decimal places

## Slide 38: Map – grid, frame and coordinates
grid properties
  type
  coordinate reference system
  interval and its unit
  style
frame properties
  type ("zebra", line with ticks, simple line)
  style settings
coordinate annotation properties
  format: decimal, DM, DMS; with or without suffix
  per side: display or not, outside/inside, rotation
  number of decimal places

## Slide 39: Map – grid, frame and coordinates
grid properties
  type
  coordinate reference system
  interval and its unit
  style
frame properties
  type ("zebra", line with ticks, simple line)
  style settings
coordinate annotation properties
  format: decimal, DM, DMS; with or without suffix
  per side: display or not, outside/inside, rotation
  number of decimal places

## Slide 40: Map – grid, frame and coordinates
grid properties
  type
  coordinate reference system
  interval and its unit
  style
frame properties
  type ("zebra", line with ticks, simple line)
  style settings
coordinate annotation properties
  format: decimal, DM, DMS; with or without suffix
  per side: display or not, outside/inside, rotation
  number of decimal places

## Slide 41: Map – grid, frame and coordinates
grid properties
  type
  coordinate reference system
  interval and its unit
  style
frame properties
  type ("zebra", line with ticks, simple line)
  style settings
coordinate annotation properties
  format: decimal, DM, DMS; with or without suffix
  per side: display or not, outside/inside, rotation
  number of decimal places

## Slide 42: Map – grid, frame and coordinates
grid properties
  type
  coordinate reference system
  interval and its unit
  style
frame properties
  type ("zebra", line with ticks, simple line)
  style settings
coordinate annotation properties
  format: decimal, DM, DMS; with or without suffix
  per side: display or not, outside/inside, rotation
  number of decimal places

## Slide 43: Map – grid, frame and coordinates
grid properties
  type
  coordinate reference system
  interval and its unit
  style
frame properties
  type ("zebra", line with ticks, simple line)
  style settings
coordinate annotation properties
  format: decimal, DM, DMS; with or without suffix
  per side: display or not, outside/inside, rotation
  number of decimal places

## Slide 44: Map – grid, frame and coordinates
grid properties
  type
  coordinate reference system
  interval and its unit
  style
frame properties
  type ("zebra", line with ticks, simple line)
  style settings
coordinate annotation properties
  format: decimal, DM, DMS; with or without suffix
  per side: display or not, outside/inside, rotation
  number of decimal places

## Slide 45: Map
DEMO
  create this map (►)
  the scale should be M 1:50 000
  apply a rotation of 5°
  add a WGS-84 coordinate grid with an interval of 0.0166666667° (1′)
  use a zebra-type frame
  display coordinate annotations at the top and on the right side with suffix, in DM format as integers

## Slide 46: Adding an inset map
a print layout may contain multiple maps
  typically complemented with a small overview inset map
  where the area shown on the main map is indicated with a rectangle
  for this, layers are usually shown or hidden depending on scale

## Slide 47: Adding an inset map
a print layout may contain multiple maps
  typically complemented with a small overview inset map
  where the area shown on the main map is indicated with a rectangle
  for this, layers are usually shown or hidden depending on scale
– COMING SOON –

## Slide 48: Adding an inset map
DEMO
  add an inset map to the upper left corner of our map with a black frame
  showing the Carpathian Basin at a scale of M 1:10 000 000
  display a thin grey grid with 1° interval and a simple frame
  and add a rectangle with a red outline

## Slide 49: Adding an inset map
DEMO
  add an inset map to the upper left corner of our map with a black frame
  showing the Carpathian Basin at a scale of M 1:10 000 000
  display a thin grey grid with 1° interval and a simple frame
  and add a rectangle with a red outline
– U G L Y ! –

## Slide 50: Adding an inset map
DEMO
  add an inset map to the upper left corner of our map with a black frame
  showing the Carpathian Basin at a scale of M 1:10 000 000
  display a thin grey grid with 1° interval and a simple frame
  and add a rectangle with a red outline
– U G L Y ! –
– R E C T A N G L E I N W R O N G P L A C E –

## Slide 51: Marking the mapped area with a rectangle
DEMO
  delete the rectangle, then load the countries.gpkg file
  display it without fill, with a thick (0.6 mm) black outline
  give meaningful names to our two maps (e.g. large map, inset map)
  add an "overview" to the inset map that shows the position of the large map without fill and with a red outline
Notes: "áttekintő"

## Slide 52: Scale-dependent rendering
DEMO
  open the properties of the places layer
  in the Rendering section enable scale dependent visibility
  display it only on maps more detailed than M 1:1 000 000
  check by zooming
  copy this style element to all other vector layers except countries
  (right click > Styles > Copy/Paste Style > Rendering)
  set the same for the digital elevation model
  refresh the maps
Notes: Megjelenítés
jobb klikk > Stílus > Stílus másolása/beillesztése > Megjelenítés

## Slide 53: Legend
DEMO
  color the railways layer based on the fclass field
  give meaningful names to the three types
  delete the other type

## Slide 54: Legend
DEMO
  add a legend to the print layout with a frame and title
  remove the countries and the base map from the legend
  rename the single layer of the elevation model to "m asl."
  create a group named "railways"
  place the railways layer in it, set it to not visible (right click > Hidden), and display feature counts
  move it before roads
  then add indentation to the group items (Spacing section)

## Slide 55: Adding other items
DEMO
  add a white-filled circle (ellipse + Shift) without outline at an arbitrary point of the map
  place a raster image file (in the example: child.jpg) in the map margin
  add a text label in a color different from black
  draw a white arrow from the text to the circle

## Slide 56: Adding other items
of course in practice we usually add
  the map title
  the author’s name
  and an institutional logo

## Slide 57: Thank you for your attention!
questions?